## Slide 1: Dipartimento di Elettronica, Informazione e Bioingegneria
Quantum Cryptography and its applications
Politecnico di Milano, 18/07/2024
2024

## Slide 2: QUANTUM CRYPTOGRAPHY AND ITS APPLICATIONS Research Project – Software Engineering 2
òòòòòòOmar Naja - DEIB
RQ1 What are the current paradigms in Quantum Cryptography?
RQ2 What are the main challenges in the field of QKD?

## Slide 3: QUANTUM CRYPTOGRAPHY AND ITS APPLICATIONS Research Project – Software Engineering 2
òòòòòòOmar Naja - DEIB

## Slide 4: BACKGROUND Quantum Mechanics principles
Photon Polarization Principle
Photons are polarized using specific filters and
resulting in one of the following polarization states
In Quantum Cryptography,
Photons are used for
transferring data
A Qubit is represented as an
unit vector in a 2-dimensional
complex vector space
A photon filter can only detect
photons with similar polarization
state, otherwise they will be
destroyed
òòòòòòOmar Naja - DEIB

## Slide 5: BACKGROUND Quantum Mechanics principles
Heisenberg Uncertainty Principle
It is not possible to calculate
accurately position and
speed of a particle
(quantum state) at the same
time: the more we are near
one of them, the less we know about the other
Planck constant
h=6,63 * 10^-34 J/Hz
òòòòòòOmar Naja - DEIB
it is inevitable to produce changes in the system if we try to calculate the quantum state of an object,
consequently, the polarization of
light particles can only be observed when it is measured

## Slide 6: BACKGROUND Quantum Cryptography
òòòòòòOmar Naja - DEIB

## Slide 7: BACKGROUND Quantum Resistant Algorithms
Focus on developing robust cryptographic systems that resist attacks from potential Quantum
Communication capabilities.
1) Code-based Algorithm: Also referred to as error correction, cryptographic schemes in this category rely on the complexity of code theory problems for signature and encryption purposes.
2) Lattice-Based Algorithm: Lattice-based encryption relies on the complexity of solving intricate mathematical problems. These algorithms generally offer robust security and efficient performance, seamlessly integrating into existing IT infrastructures.
3) Hash-based Algorithm: function H( ) that maps arbitrary-length input x on fixed-length output, h
4) Multivariate Algorithm: Based on the hardness of solving polynomial equations over a finite field
òòòòòòOmar Naja - DEIB

## Slide 8: Quantum Key Distribution QKD Introduction
2 categories of qkd protocols
Protocols based on Heisenberg’s uncertainty principle: Adversaries are detected by comparing the expected amount of error in communications between the two parties with the actual error measured.
An example of such a protocol is BB84 (attached image).
Protocols based on Quantum Entanglement:
use of entangled photon pairs shared between the two parties. Adversaries can be detected because any attempt to measure the photons will inevitably alter the entangled system.
Examples of protocols in this category include E91 or BBM92
Ciao ilo mi ciamo om
Omar Naja - DEIB

## Slide 9: Quantum Key Distribution BB84 Protocol
BB84 Stages
1) Communication process over the Quantum Channel
2) Process of communicating through the Public Channel.
a) Raw Key Generation: a phase that removes the position of the error bits (generation of a raw
cryptographic key by both parties). Here, any potential error introduced during transmission, including the positions of error bits and the bits at those positions, is identified and removed. b) Error evaluation: Both parts evaluate the errors that occurred during the raw key transmittion.
This evaluation helps ensure the accuracy and integrity of the key. c) Synchronization: The synchronization phase ensures that the users synchronize their cryptographic
systems and agree on the final key to be used for encryption and decryption. d) Privacy Amplification: This final phase involves further enhancing the security of the key by applying
privacy amplification techniques. These techniques help mitigate the impact of any potential
information leakage or eavesdropping attempts.
Ciao ilo mi ciamo om
Omar Naja - DEIB

## Slide 10: Quantum Key Distribution BB84 Protocol
The communicating parts exploit those properties to detect any attempted eavesdropping.
By encoding information in quantum states and transmitting it over quantum channels, it is easy to detect the presence of a third, malicious part attempting to intercept the communication.
This mechanism relies on the Heisenberg principle: any attempt to observe a quantum state will inevitably disturb it.
If a third party tries to intercept the communication by measuring the quantum states, his actions will inevitably alter the states, making any analysis irrelevant to his purposes.
If the level of eavesdropping is considered “acceptable” (the disturbance introduced by the eavesdropper falls below a certain threshold), the parties can proceed to generate a secure cryptographic key.
This key is guaranteed to be secure against interception by anyone not in possess of the proper quantum information.
Ciao ilo mi ciamo om
Omar Naja - DEIB

## Slide 11: Quantum Key Distribution QKDN – 6 Level architecture
òòòòòòOmar Naja - DEIB
QKDNs are communication networks in which two
users (located at two arbitrary points of the network)
can exchange symmetric keys by means of QKD
QKD nodes connected through direct point-
-to-point connections or with more complex topologies
In QKDN, quantum and classical channels
constitute the physical connection layer
(quantum layer).
However, QKDNs require a well-defined functional
and organizational architecture to provide
secret keys in various contexts.
International Telecommunication Union – Telecommunication Standardization Bureau is
currently working on defining recommendations
that cover various aspects (describing the architecture and functions, addressing their security concerns etc.). According to those recommendations, QKDNs should have a six-layered structure

## Slide 12: Quantum Key Distribution QKDN – Quantum Layer
òòòòòòOmar Naja - DEIB
The level in which secure symmetrical key is established. Here, each pair of
QKD modules connected by a QKD link
generates symmetric random bit strings.
Each QKD module pushes the (random)
bit strings up to a key manager in the
same node. Each QKD module can also
send QKD link parameters (e.g., quantum
bit error rates—QBERs, etc.) to the QKDN
manager

## Slide 13: Quantum Key Distribution QKD Links
òòòòòòOmar Naja - DEIB
LIMITS
limited quantum channel key
generation rate, available to the parties
connected by a direct optical fiber or free
line-of-sight in a point-to-point (P2P) manner over a certain distance
Necessary to secure key generation. Although fiber is commonly used for transmitting qubits,
Installation of dedicated channels for QKD
purposes is not practical in all situations.
A free space link is sometimes convenient, although it
needs lots of specific external suitable conditions
(visible light path, acceptable signal-to-noise ratio
to limit usage time...)
The QKD Link can be designated “currently unavailable” when no available key material in key storage is found, as no cryptographic operations can be performed.
Logical connection between two remote QKD nodes connected by both a quantum
channel used for transmitting photons and a public channel used for post-processing
the exchanged information, respectively [16].

## Slide 14: Quantum Key Distribution QKDN – Key Management Layer
òòòòòòOmar Naja - DEIB
This layer includes both Key Managers (KMs) and
their related links (KM links). Each KM is located in a
QKD node. The KM, connected to each other via KM links,
is used to performs key management. It receives random bit strings from the various module(s) located in
the same QKD node. The KM synchronizes and
re-formats these bit strings and stores them as
keys in the storage. The KM first receives key
requests from a cryptographic application, acquires
the necessary number of keys from storage,
synchronizes and authenticates the acquired keys
Using a KM link, and supplies them in a format
Coherent with the cryptographic application.
If KMs do not have direct links between them, they
should share the necessary number of keys via key relay. KMs, then, ask the QKDN controller(s) about a proper relay route to use for transfer the keys and finally supplies them to the cryptographic applications

## Slide 15: Quantum Key Distribution QKDN – Control Layer
òòòòòòOmar Naja - DEIB
Control functions to control QKDN resources to
ensure secure and stable QKDN operations. QKDN control functions are provided by QKDN
Controller(s).
Key function to include:
The key’s control relay routes, including rerouting
(handle cases when a failure or eavesdropping
occurs) between the two end points of the
cryptographic application, which require the key
KMs and KM links control
QKD modules and QKD links controls
Authentication and authorization control
Quality of service and charging policy control

## Slide 16: Quantum Key Distribution QKDN – Application Layer
òòòòòòOmar Naja - DEIB
Management and monitorating of the whole QKDN
system. The Application Layer manages different
Information about QKD modules and links
performances in the lower layers. Moreover, the
manager interacts with the controller aiming to support
the management and control functions of the QKDN
Key function:
Fault, accounting, configuration, performance and
security (FCAPS) management
QKDN monitoring
Support of key life cycle management in KM
Authentication and authorization management
Quality of service and charging management

## Slide 17: Quantum Key Distribution QKDN Types
òòòòòòOmar Naja - DEIB
Switched QKD Networks
Limitations on distance in point-to-point
QKD links restrict these networks to a limited scale
(metropolitan, regional).
Main drawbacks
Needs for dedicated optical infrastructure
for quantum channels, often not economically feasible.
Consistency of the applied QKD technique. Combining
different QKD techniques is not possible since no
suitable devices that could perform this transformation
are available.
Nodes connected to a dedicated optical network containing a switching mechanism to establish a direct optical point-to-point QKD connection between any two nodes in the network.
Main advantage
Reliance on an optical
switch that allows establishing connection between two nodes without active participation of other network nodes.

## Slide 18: Quantum Key Distribution QKDN Types
òòòòòòOmar Naja - DEIB
Trusted Repeaters QKD Networks
Security of each node along the transmission path is essential for securely transmitting
information.
Main advantage
Point-to-point communication between two nodes provides the same key to the nodes, enabling secure communication.
Main weakness Trusted repeater networks are not limited by distance or node numbers and can be made up of different QKD devices implementing different technologies.

## Slide 19: Quantum Key Distribution QKDN Types
òòòòòòOmar Naja - DEIB
QKD Overlay Networks
Main purpose is to achieve the higher hierarchy network to provide a better quality of service and use the resources of lower-level networks.
Independence from the paths defined by
the Internet Service Providers
The goal is to find alternative routes that
can provide service with higher quality
degrees and quick rerouting because of
Interrupt detection or multipath communications
Using multipath connections is often suggested to improve network workloads by protecting against different potential limitations (network failures, large bandwidth implementation)
public channel realization

## Slide 20: Quantum Key Distribution QKDN Types
òòòòòòOmar Naja - DEIB
QKD Overlay Networks
The overlay network connects nodes in different domains and allows usage of alternative paths by encapsulating traffic in the lower network.
When an intermediate node receives the
packet, it will be unpacked, and the
receiver’s IP address is analyzed, re-encapsulated, and forwarded
to network nodes that may be in other domains.
Considering the encapsulation principle, overlay nodes can independently perform link state measurements and guarantee fast responses to link congestion by redirecting traffic to other less-congested links.

## Slide 21: Quantum Key Distribution challenges Accuracy
òòòòòòOmar Naja - DEIB
The two communicating parts must verify that the keys are identical, as minimal noise could cause serious issues during data transmission.
To ensure accuracy without revealing the specific bits obtained, the parts can examine the parity (remainder when the sum is divided by two).
This operation can be performed publicly while keeping individual components secret.
In case groups exhibit inconsistencies, they are either rejected or divided in smaller groups, discarding or correcting at least one of them. After a proper number of repetitions, this procedure ensures that the keys are likely to be considered similar.

## Slide 22: Quantum Key Distribution challenges Security
òòòòòòOmar Naja - DEIB
Quantum mechanics enables the transmission of cryptographic keys across highly secure channels, offering a level of security unmatched by traditional methods.
The exchanged keys are unique and randomly generated, minimizing the risk of interception by any possible cyberattacker.
Additionally, during the key exchange process, polarization states are measured by both parts, resulting in the rejection of half of the bits. Furthermore, an error-correcting algorithm is employed to detect eavesdropping attempts and facilitate key regeneration.
The primary challenge faced by the system is preventing malicious users from intercepting the secret key during the exchange. QKD does not transmit the message but can produce and distribute keys that are used to encrypt and decrypt the message transmitted over a standard communication channel.

## Slide 23: Quantum Key Distribution challenges Limitations
òòòòòòOmar Naja - DEIB
Intensity of Light
The process of producing the desired polarized photons involves refining a flash source, such as a laser or a Light-Emitting Diode (LED), to ensure that each pulse consists of a single photon.
However, there are limits and challenges to consider when developing the system.
If the pulse intensity is too low, it may be imperceptible to the receiver, while an excessive intensity might make the polarity of the photon discretely identified, allowing a sleuth to read the photon from a beam concerning both the bases without any notable variance in a flash.
Both aspects – intensity and polarity – are crucial, and finding the correct balance between them is important.

## Slide 24: Quantum Key Distribution challenges Limitations
òòòòòòOmar Naja - DEIB
Time
In a cryptosystem based on Quantum Cryptography, the principle that the polarization of light or a photon particle can only be determined at the time of measurement is crucial in thwarting attempts at interception and eavesdroping

## Slide 25: Quantum Key Distribution challenges QKDN Requirements
òòòòòòOmar Naja - DEIB
Key rate
Determined by the amount of data to be
encrypted and the encryption algorithm type.
A key can be used to encrypt communication
over a public channel using an OTP cipher and
Its authentication scheme. Since an OTP requires
the same amount of key that corresponds to the
plaintext length and additional keys for its
authentication, this approach consumes more key
material than the message to transmit.
If not enough key material is available, OTP
cannot be used and the use of alternative
cryptographic techniques (AES) which does
not require a large amount of key consumption,
is the most common choice

## Slide 26: Quantum Key Distribution challenges QKDN Requirements
òòòòòòOmar Naja - DEIB
Extended distances
Enlarging the communication range of QKD systems is another key aspect for technological developments.
QKD systems based on single-photon detection champion the point-to-point communication distance and, here, the low noise of single-photon detectors is the key enabling factor
(in particular, the reachable range depends on the detectors type and operation temperature)
QKD systems transmitting over optical fiber lines face significant distance limitations compared to standard optical communication systems due to photon properties.
To overcome these limitations, researchers are exploring the concept of quantum repeaters, designed based on one of the two approaches: quantum error correction techniques or entanglement

## Slide 27: Quantum Key Distribution challenges Cost & Robustness
òòòòòòOmar Naja - DEIB
QKD systems have been shown to coexist with heavy
data traffic, eliminating the need for dark fibers (expensive and hardly available).
Access network architecture allows simultaneous access by
many QKD users; moreover, they are compatible with
full-power Gigabit Passive Optical Network traffic in the
same network.
Room-temperature single-photon detectors are suitable for DV-QKD over up to 100 km fiber, thus removing cooling requirements for the entire QKD systems, helping to
Reduce deployment cost as well as system complexity
and power consumption

## Slide 28
Omar Naja
Computer Science and Engineering - Master Student
CONTACTS
omar.naja@mail.polimi.it
THANK YOU FOR THE ATTENTION
òòòòòòOmar Naja - DEIB